Sleek Virtual Machine
January 3rd-5th 2013
Version 1
Revision 5
“Ardent”
The Sleek Virtual Machine is an innovative
programming platform, aiming to deliver to
application developers an open and crossplatform alternative to proprietary solutions.
Silas NordgrenPreface
The Sleek Virtual Machine specification was written to fully document the design of an
abstract virtual machine referred to as the Sleek Virtual Machine. This abstract virtual
machine can be implemented as a software program on a computer platform, or as a
complex instruction set computing hardware processor itself, depending on the needs of
the implementer. This document was written with these implementers in mind, and does
not refer to any particular implementation of the concepts defined within. An
implementation of the Sleek Virtual Machine must follow every rule defined in this
document; the phrases 'should' and 'should not' are to be treated as rules that require
inclusion and exclusion, respectively.
The phrase 'primarily used' defines required behavior of a feature, but this feature can
be adapted to include other functionality as long as the functionality defined after
'primarily used' is satisfied.
The phrase 'may' marks a feature not required in an implementation, but rather
allowed. The phrase 'implementers are encouraged' is a stronger version of may, where
the implementer isn't just allowed, but also encouraged and wanted to implementation
further functionality, and document it in a separate specification for possible inclusion
within the main specification of the Sleek Virtual Machine.
The phrase 'compliant implementation' refers to an implementation of the Sleek Virtual
Machine that follows all the requirements defined in this document. The phrase 'strictly
compliant implementation' refers to an implementation of the Sleek Virtual Machine that
includes no more and no less functionality than what is defined in this document.
1. Introduction
1.1. Sleek Virtual Machine
The Sleek Virtual Machine is an abstract computing machine, such as the Java
Virtual Machine, and has an instruction set just like any computer. It is tied to
the Sleek Instruction Set, which defines the rules to the input to the virtual
machine.
2. Internal Structure
The Sleek Virtual Machine has a few required internal components for proper
functionality that are used by the Sleek Instruction Set. They are documented here.
2.1. Rationale
The Sleek Virtual Machine interprets a set of bytes stored in a file format. A few
internal facilities are required to support this model of execution. They are
outlined below.
The phrase 'thread' refers to a thread of execution, a
The phrase 'global' defines a component that is the same across all threads of
the virtual machine, and it's only instance is in the main thread, while the phrase
'thread-local' defines a component that has one instance for each thread running
in the virtual machine. Thread-local components have global versions in the main
thread, however they are invisible in spawned threads, who have their own
thread-local components.
The decision to use registers primarily instead of a primarily stack-oriented
virtual machine is based on the belief that registers lead to lesser amounts of
copied values, which means more efficiency, which is part of the goal of the
Sleek Virtual Machine.
2.2. Registers
The Sleek Virtual Machine contains a set of registers manipulated by the SleekInstruction Set. These registers form the primarily variables of a program written
for the Sleek Virtual Machine. Each register holds 64 bits, but can be treated as
any 8-bit, 16-bit, 32-bit or 64-bit signed or unsigned integer, as well as a 32-bit
or 64-bit floating point value.
An implementation of the Sleek Virtual Machine may choose to implement
further registers than those supplied here. A table of the required registers can
be found in section 3.3 Registers.
The registers are global components of the Sleek Virtual Machine.
2.3. Stack
The Sleek Virtual Machine contains a stack, a last-in-first-out structure that
primarily operates on bytes and combinations of bytes.
The stack is a thread-local component of the Sleek Virtual Machine.
2.4. Constant Table
The Sleek Virtual Machine contains the ability to define constants at runtime, as
well as at compile time through a preprocessor. The constant table is a key-value
data structure that can only take.
The constant table is a thread-local component, however, each instance of the
constant table inherit the key-values found in the constant table found in the
main thread at the time of their creation.
3. Sleek Instruction Set
The Sleek Virtual Machine reads the programs that it executes from files, byte by byte.
These bytes form a program with the Sleek Instruction Set, which is a set of rules for
the bytes that are interpreted in the virtual machine. The instruction set is designed to
be compact and to not enforce impractical and inefficient restrictions on the file format,
however,
3.1. Rationale
The Sleek Virtual Machine interprets a set of bytes stored in a file format,
instead of actively interpreting source files in the language. The compiler
required to translate between source files and the set of bytes, “bytecode”,
introduces more complexity, however, a compiler need not be implemented for
each implementation of the Sleek Virtual Machine, as bytecode produced by one
compiler is not tied to any platform, unlike implementations of the virtual
machine, which require operating system-dependent calls to function.
The compiler can provide optimizations that would not be possible to do using
pure interpretation of the source, as these optimizations cannot be realistically
performed in realtime.
The use of bytecode also simplifies potential ahead-of-time compilation, where
the bytecode is translated into native code prior to runtime, as well as just-intime compilation, where the bytecode is translated into native code during
runtime. On certain processor architectures, instructions in the Sleek Instruction
Set might match one or a few processor instructions exactly, making for optimal
execution on that platform.
3.2. Concepts
The concepts behind the Sleek Instruction Set are similar to that of most other
virtual machine and processor instruction sets, albeit at a medium level ofabstraction, unlike virtual machines who often have a high level of abstraction,
and processors, who have a low level of abstraction. The Sleek Instruction Set is
designed to offer the low-level instructions for maximal results when mapping
bytecodes to native processor instructions, while offering high-level constructs
that allow for more efficiency.
3.3. Registers
The Sleek Virtual Machine contains 16 registers, that are all directly supported in
the instruction set. Quite a few of the registers serve as arguments to, or return
values from, the instructions. Each one of the registers holds 64 bits, and can be
treated as signed and unsigned integers, as well as floating point values.
Name Byte Description
ERR 0×0 The ERR register name stands for error and is primarily used to
keep track of any errors that may have occurred in the virtual
machine, or as a result of executed instructions.
PCT 0×1 The PCT register name stands for program counter and is primarily
used to keep track of the top value of the stack.
RPT 0×2 The RPT register stands for return pointer and is primarily used to
keep track of the last value that was jumped from.
SPT 0×3 The SPT register name stands for stack pointer and is primarily
used to keep track of the top value of the stack.
CTG 0×4 The CTG register name stands for callback trigger and is primarily
used to test whether or not to execute a callback subroutine.
PTS 0×5 The PTS register name stands for pointer storage and is primarily
used to pass pointers from managed and native code.
TDF 0×6 The TDF register stands for type definition and is primarily used
to distinguish between possible representations of data sent to
instructions.
EXC 0×7 The EXC register stands for exception and is primarily used to
contain pointers to exception objects.
CNC 0×8 The CNC register name stands for constant cache and is primarily
used to store the value of temporary constants on their way to and
from the constant table.
OFF 0×9 The OFF register name stands for offset and is primarily used to
hold offsets to values.
RNG 0×A The RNG register name stands for range and is primarily used to
determine exception handling offsets.
ILE 0×B The ILE register name stands for instructions left for execution
and is primarily used for executing blocks of instructions. This
register is decremented for each executed instruction.
0×C
0×D
0×E
0×F
3.4. Standard Types
The Sleek Instruction Set has an amount of generic instructions that operate
differently depending on a following bit that denotes which type of data is
incoming. Following below is a table of the bytes that are used for these
denotations.
Name Byte Description
SINT1 0×0 Signed integer of 1 byte.Name Byte Description
SINT2 0×1 Signed integer of 2 bytes.
SINT4 0×2 Signed integer of 4 bytes.
SINT8 0×3 Signed integer of 8 bytes.
UINT1 0×4 Unsigned integer of 1 byte.
UINT2 0×5 Unsigned integer of 2 bytes.
UINT4 0×6 Unsigned integer of 4 bytes.
UINT8 0×7 Unsigned integer of 8 bytes.
FTPV4 0×8 Floating point value of 4 bytes.
FTPV8 0×9 Floating point value of 8 bytes.
PTR48 0×A System pointer of 4 or 8 bytes.
3.5. Error Codes
The following is a table of error codes. The amount of error codes may be
extended in further revisions of this document.
Byte Name
0×00 UNDEFINED_ERROR
0×01 REDEFINED_CONSTANT
0×02 UNDEFINED_CONSTANT
3.6. Instructions
The following is a table of all of the 256 instructions present in the Sleek
Instruction Set. The instructions make heavy use of the internal structure of the
virtual machine.
The instruction set is divided into categories, each allocated 16 instructions. The
first category of instructions contains instructions relating to generic instructions
made on the top value of the stack.
The phrase 'generically' or 'generic' refers to a value or functionality that differs
depending on the current value of the TDF register. The implementer should
implement a separate solution for each of the possible values of the TDF
registers for each instruction.
The phrase 'immutable' refers to a value that is constant for a period of time or
permanently.
Name Byte Description
SADD 0×10 This instruction takes one argument, A. The A argument is
generically added to the top value of the stack.
SDIV 0×11 This instruction takes one argument, A. The A argument is
generically subtracted from the top value of the stack.
SMUL 0×12 This instruction takes one argument, A. The top value of the stack
is generically multiplied with the A argument.
SSUB 0×13 This instruction takes one argument, A. The top value of the stack
is generically divided by the A argument.
SINC 0×14 This instruction generically increments the top value of the stack.
SDEC 0×15 This instruction generically decrements the top value of the stack.
SSVC 0×16 This instruction takes one argument, A. The A argument is a nullterminated string of bytes. A new entry is added to the threadlocal constant table, containing the A argument and the generic top
value of the stack. If an entry with the A key already exists, thisName Byte Description
instruction sets the ERR register to the REDEFINED_CONSTANT error
value.
SLDC 0×17 This instruction takes one argument, B. The B argument is a nullterminated string of bytes. The generic result of a lookup in the
thread-local constant table is pushed to the stack. If the lookup
failed, nothing is pushed and the ERR register is set to the
UNDEFINED_CONSTANT error value.
SJMP 0×18 This instruction takes no arguments. The virtual machine sets the
RPT register to the current value of the PCT register, and the
value of the PCT register to the top value of the stack, treated as
a PTR48 value.
SREG 0×19 This instruction takes one argument, A. The virtual machine
generically sets the value of the register defined in A to the
pulled value of the stack.
SDUP 0×1A This instruction generically pushes the current top value of the
stack to the stack.
SSWP 0×1B This instruction generically pulls twice and then pushes the pulled
values in reverse order.
STPT 0×1C This instruction takes one argument, A. The virtual machine
increments the SPT register and generically sets the top value of
the stack to the value pointed at by the generic pointer A.
SFPT 0×1D This instruction takes one argument, A. The virtual machine sets
the value pointed at by the generic pointer A to the top value of
the stack and decrements the SPT register.
PUSH 0×1E This instruction takes one argument, A. The virtual machine
increments the SPT register and generically sets the top value of
the stack to the value of the register defined in A.
PULL 0×1F This instruction takes one argument, A. The virtual machine
generically sets the value of the register defined in A to the top
value of the stack and decrements the SPT register.
THRW 0×20 This instruction takes one argument, A. The virtual machine sets
the bits of the EXC register to the bits of the argument A. The
virtual machine then executes the RTHW instruction.
CTCH 0×21 This instruction takes no arguments.
FNLY 0×22 This instruction takes no arguments.
FNLZ 0×23 This instruction takes one argument, A. When the virtual machine is
exiting, the virtual machine sets the PCT register to this
instruction and
CBCK 0×24
CHCK 0×25
RTHW 0×26 This instruction takes no arguments. The virtual machine jumps to
the nearest CTCH instruction within RNG bytes and executes RNG
bytes of instructions. Then, the virtual machine jumps to the
nearest FNLY instruction within RNG bytes.
JUMP 0×27
RTRN 0×28
SUBR 0×29
JTSR 0×2A
0×2B
0×2C
0×2D
0×2E
EOIN 0×2F This byte marks the end of an instruction.